## Slide 1
Note 9 System Performance
FIT5134 Computer architecture and operating systems

## Slide 2: Outline
Computer system performance
Performance criteria
Performance enhancement
Hardware and OS performance enhancement
Example of CISC and RISC
Enhancement computer systems using the knowledge of programming
Future computer systems

## Slide 3: System Performance
Performance of computer systems has improved continually. In general, the hardware has been evolving faster than the software.
Since computer system performance is not determined solely by the CPU. One needs to consider:
  what components are involved in determining the overall system performance (eg. CPU, disks, memory, etc)?
  how can the performance of a computer system be measured (eg. Benchmarks, clock speeds, etc)?

## Slide 4: Performance Measurement
There are three common measures used to describe computer system performance:
  CPU Clock Speed – inaccurate, due to pipelining and superscalar processing (5 mhz to 3.5 Ghz over 20+years), and more recently multiple CPUs.
  MIPS (million instructions per second) - more accurate, but accuracy affected by RISC versus CISC.
  Benchmarking programs (CPU, Disk and Graphics) - most accurate for a particular task, but are task dependent.
See www.spec.org for some published benchmarks

## Slide 5: Performance Enhancements
Computer performance has been greatly enhanced by the following advancements:
  faster processing within CPU (faster CPU speed)
  multi-threading (single CPU, multiple-threads)
  multiple CPU’s (single computer, multiple CPUs)
  distributed systems (multiple co-operating computers)
  wider, faster data and instruction paths (buses)
  faster external disk access
  more (and faster) memory, including advanced cache technology. Better memory managements, such as Virtual Memory.
  faster, better quality display

## Slide 6: CPU Development
CPU speed is determined by factors such as:
  clock speed
    directly affects overall processing speed
    indirectly depends on other components to keep in sync
  instruction set architecture (or CPU architecture)
    RISC versus CISC (see later slides)
  processing technologies (see later slides)
    instruction pipelining
    scalar/superscalar processor

## Slide 7
Improving CPU Performance
Techniques to improve CPU performance:
  Use of separate Fetch and Execute instruction units, allowing concurrent fetch-execute operations
  Use of pipelining (analogy : food preparation, factory processing, etc) to overlap the fetch-execute cycles, allowing one instruction to start before another is finished
  Use of multiple/separate Execute units with a specialised Fetch unit (which can retrieve multiple instructions simultaneously), allowing parallel executions

## Slide 8
Improving CPU Performance
Pipelining overlaps the stages of the fetch-execute cycle, but completes execution of one instruction at a time. This is scalar processing.
Most modern processors also implement superscalar processing
  this uses multiple “execution units” (analogy : adding more lanes on roads to allow more traffic...) to complete the execution of several instructions at the same time (“in parallel”).
Superscalar processing is highly complex, and can have potential problems such as instructions completing in wrong order, handling program branches, and register conflicts.

## Slide 9: Using Cache memory
A ‘small’ amount of fast memory between the CPU and primary memory.
All memory references are checked against the cache, and the cache location used if the memory reference occurs in one of the cache blocks.
For a 64Kbyte cache, hit ratios of 90% or more can be achieved, with execution speed improvements of 50% or more.

## Slide 10: Using Cache memory
Reading is simple – just retrieve from cache
Writing is more difficult, because writes must be made to primary memory to preserve the integrity of the contents of primary memory.
  generally two strategies:
    1. Write Through – write all changes directly to primary memory
    2. Write Back – only write changed data when it is to be evicted from cache

## Slide 11: Other components affecting overall system performances
Disks
  increased speeds, use of caches, efficient scheduling, etc
Bus
  increased width and speed of paths for data and instructions, faster speeds, etc
Display
  faster graphics cards, more onboard memory, better panel technologies, etc

## Slide 12: CISC vs RISC CPU architectures
  CISC (complex instruction set computers)
    eg. IBM mainframes, Intel x86
    characteristics : small number of registers, large number of specialised instructions, variable instruction word sizes.
    more recent CISC processors use a combination of pipelining, superscalar and RISC technologies to increase throughput.
  RISC (reduced instruction set computers)
    eg. PowerPC, Sun SPARC
    characteristics : larger number of registers, smaller number of specialised instructions, fixed instruction word size.

## Slide 13: CISC vs RISC CPU architectures
  With advancement in computer architecture, CISC and RISC seem to have adopted each other’s strategies.
  Some features in RISC are better than CISC and via versa, depending what sort of programs the computer runs.
  Researchers try to select best features of each architecture and improve both hardware and OS in order to build faster computer.

## Slide 14: Procedure Calls
generally very time consuming
depends on number of parameters passed
depends on level of nesting
For some programming language like C or C++, there are many procedure calls in large programs since it is hard to read a long C procedure

## Slide 15: Implications?
best support (for procedure calls) is given by optimising the most used and most time-consuming features:
  provides larger number of registers
  careful design of instruction pipelines (how instruction executions can be overlapped)
  simplified (reduced) instruction set

## Slide 16: Future Computer Systems
Parallel computers and multi-state computer systems such as quantum computers are the way
OS can be improved or rewritten to work with new architectures
There are many programming languages with concurrency features. They can be improved to work well with new architectures.